## Slide 1
DESIGN AND SIMULATION OF AN
AUTOMATIC STREET LIGHT
CONTROL SYSTEM
Digital Logic Design using Logisim
LDR / Light Sensor + Motion Sensor → Logic Circuit → Street Lamp
PROJECT TEAM
Toshita — 2620030361
Aparna — 2620030367
Sushma — 2620030374
Manasi — 2620030380
Vinay — 2620030387

## Slide 2
INTRODUCTION AND OBJECTIVE
02 / 06
• Street lights improve safety and visibility during dark conditions.
• Manual switching can waste energy when lights are left ON unnecessarily.
• The LDR/light sensor represents day or night, while a motion sensor detects activity.
• Objective: design and simulate an automatic controller using basic digital logic gates in Logisim.
• The lamp output is controlled by the Boolean expression: Light = ¬L + M.

## Slide 3
THEORY AND LOGIC CIRCUIT
03 / 06
INPUTS
L = 1 for Day, 0 for Night
M = 1 when motion is detected
BOOLEAN LOGIC
Night = ¬L
Light = ¬L + M
GATES USED
NOT gate: converts Day to Night
OR gate: turns the lamp ON if it is night or motion is detected.
L (Day)
NOT
M (Motion)
OR
LIGHT OUTPUT
Lamp ON / OFF
Circuit concept: invert L to obtain Night, then OR it with M.

## Slide 4
CIRCUIT DESIGN IN LOGISIM
04 / 06
• Place two input pins/switches and label them L (Day) and M (Motion).
• Connect L to a NOT gate to produce ¬L (Night).
• Connect ¬L and M to the two inputs of an OR gate.
• Connect the OR output to an LED or lamp indicator.
• Toggle the input switches to test the output against the truth table.
L
NOT
¬L
M
OR
LIGHT

## Slide 5
SIMULATION RESULTS
05 / 06
Truth Table
L (Day) | M (Motion) | Light Output
0 | 0 | 1 (ON)
0 | 1 | 1 (ON)
1 | 0 | 0 (OFF)
1 | 1 | 1 (ON)
Test cases
• Night + no motion → ON
• Night + motion → ON
• Day + no motion → OFF
• Day + motion → ON
Equation: Light = ¬L + M
In Logisim, toggle both inputs and verify that the lamp matches each row.

## Slide 6
CONCLUSION AND APPLICATIONS
06 / 06
CONCLUSION
• The controller demonstrates automatic street-light operation using simple digital logic.
• The LDR represents day/night conditions, while the motion sensor represents detected activity.
• The Boolean expression Light = ¬L + M determines the lamp output.
• The circuit can be tested and verified in Logisim.
APPLICATIONS
• Public roads and highways
• College and school campuses
• Parking areas and residential streets
• Smart-city and building security lighting
Possible improvement: add a timer, dimming control, or extra sensors.